## Slide 1
Terrestrial CO2 fluxes, concentrations, and budgets
in USA and Northeast China
Xiao-Ming Hu1, and Xiaolan Li2
http://www.caps.ou.edu/~xhu/
2019-06-27 @ Peking Univ.
1Center for Analysis and Prediction of Storms, and School of Meteorology, University of Oklahoma
2Institute of Atmospheric Environment, China Meteorological Administration, Shenyang

## Slide 2: CO2-induced global warming?

## Slide 3
Trend of CO2
Park Falls, TCCON
Remote sensing
In situ
Global warming controversial? Look at CO2 trend!!
In situ

## Slide 4
Terrestrial CO2 fluxes
IPCC (2007)
Global CO2 sources and sinks
Uncertainties of terrestrial CO2 fluxes are large

## Slide 5
Terrestrial CO2 fluxes in different regions
Uncertainties in each region/plant function are large too
King et al., 2012

## Slide 6
WRF/Chem-VPRM for CO2 simulation
Vegetation Photosynthesis and Respiration Model (VPRM) (Xiao et al., 2004; Mahadevan et al., 2008; Ahmadov et al., 2007)

## Slide 7: Implemented parameters from Hilton, Davis et al. (2013)
 | Evergreen forest | Deciduous forest | Mixed forest | Shrub | Savanna | Crop | Grass
 | 745.306 | 514.13 | 419.5 | 590.7 | 600 | 1074.9 | 717.1
 | 0.13 | 0.1 | 0.1 | 0.18 | 0.18 | 0.085 | 0.115
 | 0.1247 | 0.092 | 0.2 | 0.0634 | 0.2 | 0.13 | 0.0515
 | 0.2496 | 0.843 | 0.27248 | 0.2684 | 0.3376 | 0.542 | -0.0986
 | Evergreen forest | Deciduous forest | Mixed forest | Shrub | Savanna | Crop | Grass
 | 745.306 | 514.13 | 419.5 | 590.7 | 600 | 1074.9 | 717.1
 | 0.13 | 0.1 | 0.1 | 0.18 | 0.18 | 0.085 | 0.115
 | 0.1247 | 0.092 | 0.2 | 0.0634 | 0.2 | 0.13 | 0.0515
 | 0.2496 | 0.843 | 0.27248 | 0.2684 | 0.3376 | 0.542 | -0.0986
And other minor changes to VPRM in WRF
Calibrated using eddy covariance tower data over North America

## Slide 8: Downscaling in year 2016 from CT-NRT.v2017
WRF-VPRM IC
Point 1: both IC/BC are time dependent
Point 2: resolution of WRF-VPRM is much higher, adequate to investigate impact of weather

## Slide 9: configuration for WRF-VPRM downscaling
Short wave radiation | Dudhia
Long wave radiation | rapid radiative transfer model (RRTM)
Boundary layer | YSU
Microphysics | Morrison
Cumulus | Grell-Freitas
Land surface model | NOAH
Vertical levels | 47
Horizontal resolution | 12 km  12 km with 266443 grid points
Time step | 60 seconds
Meteo initial and lateral boundary conditions | NCEP/DOE Reanalysis 2 (R2)
CO2 initial and lateral boundary conditions | CarbonTracker global simulation 3o2o outputs
Interior nudging | Spectral nudging
nudging variables | horizontal wind components, temperature, geopotential
nudging coefficient | 310-5 s-1
nudging height | above PBL
wave number | 5 and 3 in the zonal and meridional directions respectively
nudging period | throughout the downscaling simulation

## Slide 10
Downscaling captures the monthly variation of precipitation

## Slide 11
Biogenic CO2 fluxes downscaled by WRF-VPRM vs. CarbonTracker posterior fluxes
CT2017
WRF-VPRM

## Slide 12: XCO2 at the 4 TCCON sites
captures the seasonal and some episodic variation of XCO2.
Bias in western boundary?
Bias in anthropogenic emission?

## Slide 13: Evaluation of CT2017
Evaluation of WRF-VPRM
Thus, bias in western boundary partially contributed to WRF-VPRM bias?

## Slide 14: Individual contribution to XCO2

## Slide 15: Compare with OCO-2; individual contributions
Total
Biogenic
Anthropogenic
Background

## Slide 16: Compare with OCO-2, individual cases

## Slide 17: Statistic evaluation of XCO2 using OCO-2 data
Best performance in Summer, followed by Fall

## Slide 18: Case study July 25
Capture the contrast across boundary layer top

## Slide 19: Case study, Aug 5 OCO-2 underpass

## Slide 20: Aug 21,2016
Capture the contrast across boundary layer top,
and across cold front

## Slide 21: Summary
Calibrated VPRM parameters from Hilton et al [2013] are implemented into WRF-VPRM
WRF-VPRM reasonably captures monthly variation of XCO2 and episodic variations due to frontal passages
The downscaling also successfully captures the horizontal CO2 gradients across fronts, as well as vertical CO2 contrast across the boundary layer top.

## Slide 22
Terrestrial CO2 fluxes in different regions
Uncertainties in each region are large too
Asia is CO2 sink!!

## Slide 23
Mixed forest and cropland dominate in Northeast China
Crop area is still increasing!!
SIF: Sun-induced Fluorescence, proportional to photosynthesis
Northeast China: a major CO2 sink
MODIS vegetation type

## Slide 24
Observational parameters:
  1) Hourly mean CO2 fluxes and concentrations,
  2) wind speed and direction, air temperature
  3) PAR (only at Fujin)
Observational period:
  Fujin: since 2012
  Wuying: since 2014
Fujin, rice paddy field
(129.2661°E, 48.2991°N, 59 m)
Wuying, mixed forest site
(131.9385°E, 47.1519°N, 345 m)
Long-term tower measurements, focusing on 2016

## Slide 25
Resolution: 20 km in d01; 4 km in d02
Meteorology initial/boundary conditions: NECP/DOE R2
CO2 initial/boundary conditions: 3o×2o CarbanTracker 2017
Anthropogenic emissions of CO2: ODIAC
2016 downscaling using WRF-VPRM: a weather-biosphere-online-coupled model
Following Hu et al. (2019) based on Hilton et al. (2013)
maximum light use efficiency
photosynthetically active radiation
Related to land surface water index (LSWI)
Roughly equal to enhanced vegetation index (EVI)
phenology
scale
water stress scale

## Slide 26
OCO-2 retrieved XCO2 (L2 Lite Version 9)
Advantage: spatiotemporal coverage
Disadvantage: interfere with cloud and haze pollution!!

## Slide 27
Seasonal variations of CO2 fluxes and concentrations
Fujin (cropland, rice paddy)
R = 0.98
R = 0.87
MODIS vegetation type
Notes: 1) correlation between EVI and NEE; 2) seasonal variation of NEE and CO2 concentrations

## Slide 28
Bias of terrestrial respiration
Fujin (cropland, rice paddy)
R = 0.98
R = 0.87
largely subjected to the EVI
Ignores leaf mass, involves EVI?
Notes: 1) correlation between EVI and NEE; 2) seasonal variation of NEE and CO2 concentrations

## Slide 29
Seasonal variation of CO2 fluxes and concentrations
Wuying (mixed forest)
R = 0.99
MODIS vegetation type

## Slide 30
R = 0.99
Episodic variation on October 15, 2016
Wuying (mixed forest)
Fujin (cropland, rice)
Notes: 1) correlation between EVI and NEE; 2) seasonal variation of NEE and CO2 concentrations

## Slide 31
Anthropogenic emissions & biogenic contribution
Anthropogenic emissions only
Anthropogenic contribution: 59.4 ± 5.9% Biogenic contribution: 40.6 ± 5.9%
Regional transport on October 15

## Slide 32
Regional transport as well as subsidence?
Vertical cross-section on October 15

## Slide 33
OCO-2 retrieved XCO2 (L2 Lite Version 9)
Advantage: spatiotemporal coverage
Disadvantage: interfere with cloud and haze pollution!!

## Slide 34
Seasonal variation of XCO2 over Northeast China
Seasonal variation range: 10 ppmv
Annual mean contribution:
anthropogenic: 0.84 ppmv
biogenic: -0.60 ppmv
Weak winds favors the large anthropogenic contribution of XCO2 in summer
32% lower than the annual level

## Slide 35
Mean diurnal variation of CO2 fluxes and concentrations in growing season
WRF-VPRM underestimates diurnal variation range over mixed forest
Wuying (mixed forest)
Fujin (cropland, rice paddy)

## Slide 36
Ensemble offline VPRM simulations over mixed forest, predictability of CO2 fluxes

## Slide 37: Conclusions and future work
Mixed forest is observed as a stronger CO2 sink/source than rice paddy on average in 2016;
Negative biogenic contribution offset about 70% of anthropogenic contribution of XCO2 over Northeast China in 2016;
The uncertainty of NEE simulation largely depends on four VPRM parameters, especially the maximum light use efficiency λ.
=
EVI
1.25*(EVI-0.1)
Also separate crop into C3/C4
Future: Update VPRM in WRF, including update the GEE equation and parameters.

## Slide 38: CO2 models
Global models:
  Chemistry transport model TM3 (Heiman, 1996), TM5 (Krol et al., 2005)
  Laboratoire de Met´eorologie Dynamique, LMDZ（Hauglustaine et al., 2004）
  ECHAM-4 (Max Planck Institute for Meteorology)
  CarbonTracker (only simulate CO2 fluxes, not CO2 concentrations)
Regional models:
  NCAR episodic regional chemical transport mode, HANK（Hess et al., 2000）
  Danish Eulerian Hemispheric Model, DEHM (Christensen, 1997)
  REgional MOdel, REMO(Majewski, 1991)
  DEHM-LSM (land surface model), (Geel et al., 2004)
  RAMS-SiB2(Scott Denning et al., 2003)
Reference: https://www.atmos-chem-phys.net/7/3461/2007/acp-7-3461-2007.pdf